## Slide 1: MAmidiMEmo The Virtual S/W Synthesizer
User’s Manual - Rev 0.6.0

## Slide 2: What is the MAmidiMEmo?
MAmidiMEmo is a virtual chiptune sound MIDI module for Windows
You can use MIDI or DAW to sound the MAmi
MAmi supports various sound chips*
Also, MAmi can drive real hardware chips* via SCCI, VSIF
- DAW
- MIDI Sequencer
- Tracker
- MML and so on…
- MIDI Inst
* Supported chips are the following
PCM: C140, SPC700
FM Synthesis: OPM, OPN2, OPNA, OPLL, OPL, OPL3
WSG: NAMCO CUS30, HuC6280, SCC
PSG: SID, POKEY, GB APU, SN76496, NES APU, MSM5232, AY-3-8910
VOICE: TMS5220, SP0256, SAM
MIDI: MT-32, CM-32P(Simlation)
YM2612
YM2612
YM2612
S/W Chips
YM2612
YM2612
YM2612
Real Chips
Sound Driver
SCCI/VSIF
* Supported hardware is the following
VSIF: Genesis, SMS, Famicom, MSX
SCCI: OPM, OPNA

## Slide 3: Install & Basic Settings
Install
  Extract the downloaded zip file.
  Click MAmidiMEmo.exe
  Will open the MAmidiMEmo. If not, please check the followings.
    .NET Framework 4.7 or later installed on your PC.
    VC++ 2012 Runtime installed on your PC.
    (Execute "DelZoneID.ps1“ to remove “Zone.Identifier” flag.)

## Slide 4: Window Overview
MIDI IN A,B
Selector
Active Chips
(see next)
Chip Parameter Editor
(see next)
Tools

## Slide 5: Add and Remove a Chip
To add
Select the chip from this menu.
To remove
Open a context menu and select.

## Slide 6: Edit chip and sound parameters
1. Click chip
2. Click parameter
3. Change value

## Slide 7: Between MIDI ch and Chip ch Relation.
You don’t need to concern the Chip ch. , generally. MAmidiMEmo will assign suitable Chip ch. automatically. However, you need to concern a max ch. number of the Chip.
MAmidiMEmo will assign oldest sounding ch. to sound the new sounds.
Note On Msg from
MIDI ch. X
Chip A
FM ch. 1
FM ch. 2
FM ch. 3
MAmidiMEmo
MAmidiMemo will assign empty ch. or oldest sounsing ch. , generally.

## Slide 8: Sounding Structure
MAmidiMEmo outputs a sound from MIDI message along with the following structure. So, at least, you need to edit the Timbre parameters to sound something.
Chip X
MIDI IN
Chip A
[MIDI]-[MidiPort]
[MIDI]-[Channels]
[MIDI]-[ProgramAssignments]
[MIDI]-
[ChannelTypes]
Timbre
CombinedTimbre
DrumTimbre

## Slide 9: Timbre
Generally, a chip has 256 Timbres, 256 CombinedTimbres, 128 DrumTimbres.
CombinedTimbre can sound multiple Timbers at the same time (up to 4)
DrumTimbre can sound Timbes as a Drum sounds (Ignoring Note Off msg).
You can change the Timbre parameters on the Chip Parameter Editor. Generally, you need to learn the chip specification to edit the chip parameters.
Chip Parameter Editor

## Slide 10: Timbre Structure
Chip
CombinedTimbre
Timbre
Timbre
Timbre
Timbre
Timbres
DrumTimbre
Timbre
DrumTimbres
Timbre
CombinedTimbres
Timbre
Timbre
Timbre
Timbre
Sound parameter
Driver parameter
MIDI parameter
Sound parameter
FM Op parameters
PSG parameters
PCM parameters
Driver parameter
ADSR parameter
ARP parameter
Fx & Env parameter
Sound params are H/W settings.
See the chip manual for more details.
Driver params are the MAmidiMEmo settings.

## Slide 11: Driver parameters - Fx & Env Structure
Fx & Env parameter
Volume Env
Pitch Env
Arp Env
Dedicated Env
Click here to open the GUI Editor.
You can make for a rich sound by using driver params. Especially, FxS can do it.

## Slide 12: Sample sounds
There are sample sound files in the “Samples” folder. You can drop a sample file “*.MAmi" to the left pane.

## Slide 13: Additional files
YM2608
  Place legitimate “ym2608_adpcm_rom.bin” file in the MAmidiMEmo directory to sound ADPCM rhythm sounds.
MT-32
  Place legitimate “MT32_CONTROL.ROM” and “MT32_PCM.ROM” in the MAmidiMEmo directory to sound ADPCM sounds.

## Slide 14: Limit Break
Any chip can output only a few voices. However, MAmidiMEmo can break this limitation by the following steps.
  Add a chip and complete all settings the chip.
  Select the [Clone selected chip] Cloned chip added.
  Select the cloned chip and set the [Follower Mode] value to “Unit0*”. * If clone source chip ID is 0.
When the clone source chip consumed all voices, the cloned chip sound for the chip.
If you want to extend max voices more, select the [Clone selected chip] of the cloned chip. And set the [Follower Mode] value to “Unit0”.

## Slide 15: VGM Sound Interface(VSIF - UART) for Genesis/SMS
MAmidiMEmo and VGMPlayer can drive real machine chips. Currently supports NTSC SMS(2, MkⅢ) for SN76489, OPLL and NTSC Genesis(MD) for SN76489, OPN2.
How to
  Buy the following parts. ・1x UART dongle (Note: FT232R and so on. CH340 and CP2102 may not work 163,840bps, only 115,200bps.) ・1x FLASH Cart for SMS or Genesis and 1x D-SUB 9 pin female connector and DuPont wires
  Solder like the following.
SMS/2 or MkⅢ
Genesis/MD
Any UART dongle
*Need to support
163,840bps for MD
115,200bps for MD, SMS

## Slide 16: VGM Sound Interface(VSIF - FTDI) for Genesis
MAmidiMEmo and VGMPlayer can drive real machine chips more faster if you use FTDI2xx(232R, 232H and so on). Currently supports NTSC Genesis(MD) for SN76489, OPN2.
How to
  Buy the following parts.
    ・1x FTDI2XX dongle (FT232R and so on. Need to support 5V.) ・1x FLASH Cart for Genesis and 1x D-SUB 9 pin female connector and DuPont wires
  Solder like the following.
Genesis/MD
Any FTDI2XX dongle
DTR
DSR
DCD

## Slide 17: VGM Sound Interface(VSIF - FTDI) for Famicom
MAmidiMEmo can drive real machine chips more faster if you use FTDI2xx(232R, 232H and so on). Currently supports NTSC Famicom and RP2A03(No DAC)/FDS/VRC6.
How to
  Buy the following parts.
    ・1x FTDI2XX dongle (FT232R and so on. Need to support 5V.) ・1x FLASH Cart for Famicom and 1x D-SUB 15 pin female connector for FC and DuPont wires
  Solder like the following.
Famicom
Any FTDI2XX dongle
DTR
Audio
(Optional)

## Slide 18: VGM Sound Interface(VSIF - FTDI) for MSX
MAmidiMEmo can drive real MSX machine chips if you use FTDI2xx(232R, 232H and so on). Currently supports NTSC MSX for AY-3-8910 and OPLL and SCC+ and OPL3. NOTE: Be sure to select proper SLOT# for SCC to use SCC.
How to
  Buy the following parts.
    ・1x FTDI2XX dongle (FT232R and so on. Need to support 5V.) ・1x D-SUB 9 pin female connector and DuPont wires
  Solder like the following to the JOYSTICK PORT 2.
MSX
Any FTDI2XX dongle
DTR
DSR

## Slide 19: VGM Sound Interface(VSIF) Settings
Burn VGMPlay_md.bin(for Genesis) or VGMPlay_sms.sms(for SMS) or VGMPlay_nes*.* (for Famicom) or VGMPlaymsx.rom/bin(for MSX) to your FLASH Cart.
  *VGMPlay_nes_vrc6/fds/mmc5 ROM does not show any screen but same UI with VGMPlay_nes.nes UI
Set the COMPort/FTDI ID and select “VSIF ***” you wish.
Reset your console and push [Panic!] button
(Famicom only)Re-send DPCM data.
Done!
If you can not sound sounds, make sure soldering and COMPort name. Or, please contact me. *Some UART dongles may not work properly. *Compatible consoles may not work properly.

## Slide 20: VGM Sound Interface(VSIF) for Famicom spec
Sound | Normal ROM (Mapper 0) | FDS IMAGE*2 | VRC6 ROM*2 (Mapper 24) | MMC5 ROM*2*3 (Mapper 5)
Square | OK | OK | OK | OK
Tri | OK | OK | OK | OK
Noise | OK | OK | OK | OK
DPCM | NO | OK(Up to 8KB) | NO | OK*1 (Up to 64KB)
Ext. Snd FDS | NO | OK*1 | NO | NO
Ext. Snd VRC | NO | NO | OK*1 | NO
Ext. Snd MMC | NO | NO | NO | NO
*1 Not Tested
*2 China flash cart may not work properly
*3 PRG-RAM 32x2 KB

## Slide 21: VGMPlayer
Select interface type
NOTE: Bandwidth of UART is narrow. So you can not play heavy track data properly.
3) Check to connect
NOTE: If you re-connect to FTDIxxx mode, please reset Gen/MD.
5) Adjust CLK speed for FTDIxxx mode for each environment (7～8% is best for normal machine)
6) Adjust buffer size for each files. (0 is max accuracy but so heavy.)
2) Select interface ID
for UART: COMPort#
for FTDI2xxx: FDTI ID#

## Slide 22: Trouble Shooting for MAmi
If you noticed “sound lag” or “stutter”, open the Settings dialog from [TOOL] menu. Check [Sound Type] and [Audio Latency] value.

## Slide 23: MIDI Implementation Chart 1
Function | Transmitted | Recognize | Remarks
Basic Channel | - | 1-16: Defaut 1-16: Changed | 
Note Number* | - | 0-127 | 
Velocity* | - | Yes: Note ON No: Note OFF | 
After Touch | - | No | 
Pitch Bend* | - | Yes | 8192: Default
Program Change | - | 0-127 | 0: Default
*Depends on the chip

## Slide 24: MIDI Implementation Chart 2
Function | Transmitted | Recognize | Remarks
Control Change 1 | - | Modulation | 0: OFF, 64: ON
5 |  | Portamento Time | 0: Default
6 38 |  | Data Entry MSB Data Entry LSB | 
7 |  | Volume* | 127: Default
10 |  | Panpot* | 64: Default 0: Left, 127: Right
11 |  | Expression* | 127: Default
16-19 |  | GPCS1 | Modify params
64 |  | Hold 1 | 0: OFF, 64: ON
65 |  | Portamento | 0: OFF, 64: ON
*Depends on the chip

## Slide 25: MIDI Implementation Chart 3
Function | Transmitted | Recognize | Remarks
Control Change 70-75,79 | - | SCCS | Modify current timbre params
76 77 78 | - - - | Mod. Rate Mod. Depth Mod. Delay | 64: Default 64: Default 64: Default
80-83 | - | GPCS2 | Modify parameters
84 | - | Portamento Ctrl | 0: OFF, 64: ON
91-95 | - | VST Plugin Ctrl | Modify VST params
98 99 | - - | NRPN LSB NRPN MSB | 
100 101 | - - | RPN LSB RPN MSB | 
*Depends on the chip

## Slide 26: MIDI Implementation Chart 4
Function | Transmitted | Recognize | Remarks
Control Change 121 | - | Reset All Ctrl | 
126 | - | Mono Mode | 0: OFF 1-127: Max Voice Num.*
127 | - | Poly Mode | 0: OFF 1-127: Reserve Voice Num.* *Reset Mono Mode when set
*Depends on the chip

## Slide 27: MIDI Implementation Chart 5
Function | MSB | LSB | Remarks
RPN | 0 | 0 | Pitch Bend Range 0-2-127 [Half Note]
 | 0 | 5 | Mod Depth 0-127 [Relative]

## Slide 28: MIDI Implementation Chart 6
Function | MSB | LSB | Remarks
NRPN | 0 | 16-19 80-83 | GPCS[1-4] Value GPCS[5-6] Value 0-127
 | 0 | 70-75 79 | SCCS[1-6] Value SCCS[10] Value 0-127

## Slide 29: MIDI Implementation Chart 7
Function | Change Receiving MIDI ch. dynamically. | Remarks
NRPN | NRPN MSB Bx 63 41 … for MIDI ch(1-7) NRPN LSB Bx 62 <Device ID> ... Specify Device ID of existing instrument. DATA MSB Bx 26 <Unit No> ... Specify Unit No of the above Device ID of existing instrument. DATA LSB Bx 06 <Receiving MIDI ch(1-7) bit sets. 1=On, 0=Off> bit 6 5 4 3 2 1 0 ch 7 6 5 4 3 2 1 NRPN MSB Bx 63 42 ... for MIDI ch(8-14) NRPN LSB Bx 62 <Device ID> ... Specify Device ID of existing instrument. DATA MSB Bx 26 <Unit No> ... Specify Unit No of the above Device ID of existing instrument. DATA LSB Bx 06 <Receiving MIDI ch(8-14) bit sets. 1=On, 0=Off> bit 6 5 4 3 2 1 0 ch 14 13 12 11 10 9 8 NRPN MSB Bx 63 43 ... for MIDI ch(15-16) NRPN LSB Bx 62 <Device ID> ... Specify Device ID of existing instrument. DATA MSB Bx 26 <Unit No> ... Specify Unit No of the above Device ID of existing instrument. DATA LSB Bx 06 <Receiving MIDI ch(15-16) bit sets. 1=On, 0=Off> bit 6 5 4 3 2 1 0 ch xx xx xx xx xx 16 15 | 

## Slide 30: VSIF – Generic (UART 115K), SMS(UART 115K) SPECIFICATION for AY-3-8910, YM2413
Baud rate: 115,200 bps
Protocol: 8 bits, None parity bit, 1 stop bit
1 packet : 2 bytes
Reg #
Value
1st
2nd

## Slide 31: VSIF – MSX(FTDI) SPECIFICATION for AY-3-8910, YM2413, SCC-I, YMF262
Baud rate : 38,400 bytes / sec
1 packet : 5 bytes
1byte : 4bit(data) + 2bit(Start + Clk bit)
Type:
  0 AY-3-8910: Write value to address
  1,2 YM2413: 1 is write value to address, 2 is set OPLL cartridge slot number
  3～9 SCC-I: (in preparation)
  10～11 YMF262: 10 is write value to address of port L , 11 is Write value to address of port H
Address(Hi)
Address(Lo)
Value(Lo)
Value(Hi)
Type
1st
2nd
3rd
4th
5th
Start
Clk
Data
Data
Data
Data
LSB
0
MSB
7