## Slide 1: MAmidiMEmo A Virtual S/W Synthesizer
User’s Manual - Rev 0.3

## Slide 2: Install & Basic Settings
Install
  Extract the downloaded zip file.
  Click MAmidiMEmo.exe
  Will open the MAmidiMEmo. If not, please check the followings.
    .NET Framework 4.7 or later installed on your PC.
    VC++ 2012 Runtime installed on your PC.
    (Execute "DelZoneID.ps1“ to remove “Zone.Identifier” flag.)

## Slide 3: Window Overview
MIDI IN A,B
Selector
Active Chips
(see next)
Chip Parameter Editor
(see next)
Tools

## Slide 4: Add and Remove a Chip
To add
Select the chip from this menu.
To remove
Open a context menu and select.

## Slide 5: Edit chip and sound parameters
1. Click chip
2. Click parameter
3. Change value

## Slide 6: Between MIDI ch and Chip ch Relation.
You don’t need to concern the Chip ch. , generally. MAmidiMEmo will assign suitable Chip ch. automatically. However, you need to concern a max ch. number of the Chip.
MAmidiMEmo will assign oldest sounding ch. to sound the new sounds.
Note On Msg from
MIDI ch. X
Chip A
FM ch. 1
FM ch. 2
FM ch. 3
MAmidiMEmo
MAmidiMemo will assign empty ch. or oldest sounsing ch. , generally.

## Slide 7: Sounding Structure
MAmidiMEmo outputs a sound from MIDI message along with the following structure. So, at least, you need to edit the Timbre parameters to sound something.
Chip X
MIDI IN
Chip A
[MIDI]-[MidiPort]
[MIDI]-[Channels]
[MIDI]-[ProgramAssignments]
[MIDI]-
[ChannelTypes]
Timbre
CombinedTimbre
DrumTimbre

## Slide 8: Timbre
Generally, a chip has 256 Timbres, 256 CombinedTimbres, 128 DrumTimbres.
CombinedTimbre can sound multiple Timbers at the same time (up to 4)
DrumTimbre can sound Timbes as a Drum sounds (Ignoring Note Off msg).
You can change the Timbre parameters on the Chip Parameter Editor. Generally, you need to learn the chip specification to edit the chip parameters.
Chip Parameter Editor

## Slide 9: Timbre Structure
Chip
CombinedTimbre
Timbre
Timbre
Timbre
Timbre
Timbres
DrumTimbre
Timbre
DrumTimbres
Timbre
CombinedTimbres
Timbre
Timbre
Timbre
Timbre
Sound parameter
Driver parameter
MIDI parameter
Sound parameter
FM Op parameters
PSG parameters
PCM parameters
Driver parameter
ADSR parameter
ARP parameter
Fx & Env parameter
Sound params are H/W settings.
See the chip manual for more details.
Driver params are the MAmidiMEmo settings.

## Slide 10: Driver parameters - Fx & Env Structure
Fx & Env parameter
Volume Env
Pitch Env
Arp Env
Dedicated Env
Click here to open the GUI Editor.
You can make for a rich sound by using driver params. Especially, FxS can do it.

## Slide 11: Sample sounds
There are sample sound files in the “Samples” folder. You can drop a sample file “*.MAmi" to the left pane.

## Slide 12: Additional files
YM2608
  Place legitimate “ym2608_adpcm_rom.bin” file in the MAmidiMEmo directory to sound ADPCM rhythm sounds.
MT-32
  Place legitimate “MT32_CONTROL.ROM” and “MT32_PCM.ROM” in the MAmidiMEmo directory to sound ADPCM sounds.

## Slide 13: Limit Break
Any chip can output only a few voices. However, MAmidiMEmo can break this limitation by the following steps.
  Add a chip and complete all settings the chip.
  Select the [Clone selected chip] Cloned chip added.
  Select the cloned chip and set the [Follower Mode] value to “Unit0*”. * If clone source chip ID is 0.
When the clone source chip consumed all voices, the cloned chip sound for the chip.
If you want to extend max voices more, select the [Clone selected chip] of the cloned chip. And set the [Follower Mode] value to “Unit0”.

## Slide 14: VGM Sound Interface(VSIF) – (1)
MAmidiMEmo can drive real machine chips. Currently supports NTSC SMS(2, MkⅢ) for SN76496/OPLL and NTSC Genesis(MD) for SN76496/OPNA2.
How to
  Buy the following parts.
    1x UART (FT232R and so on. But CH340 may not) dongle (Note: Supports 163,840bps, 115,200bps)
    1x FLASH Cart for SMS or Genesis and 1x D-SUB 9 pin connector (Female) and DuPont wires
  Solder like the following.
SMS/2 or MkⅢ
Genesis/MD
Pin3 - TX, Pin8 - GND
Pin1 - TX, Pin8 - GND
Any UART dongle
*Supports
163,840bps
115,200bps

## Slide 15: VGM Sound Interface(VSIF) – (2)
Burn VGMPlay_md.bin(for Genesis) or VGMPlay_sms.sms(for SMS) to your FLASH Cart
Set the COMPort name and select “VSIF SMS” or “VSIF Genesis”.
Done!
If you can not sound sounds, make sure soldering and COMPort name. Or, please contact me.

## Slide 16: VGM Sound Interface(VSIF FTDI) for VGM Player
VGM Player can drive real machine chips more faster if you use FTDI2xx(232R, 232H and so on). Currently supports NTSC Genesis(MD) for SN76496/OPNA2.
How to
  Buy the following parts.
    1x FTDI2XX (FT232R and so on) dongle
    1x FLASH Cart for Genesis and 1x D-SUB 9 pin connector (Female) and DuPont wires
  Solder like the following.
Genesis/MD
Any FTDI2XX dongle
DTR
DSR
DCD

## Slide 17: VGMPlayer
Select interface type
NOTE: Bandwidth of UART is narrow. So you can not play heavy track data properly.
2) Select interface ID
COMPort # for UART
FDTI ID# for FTDI2xxx
3) Connect
NOTE: If you re-connect to FTDIxxx mode, please reset Gen/MD.
5) Adjust CLK speed for FTDIxxx mode for each environment ( 7～8% is best for normal machine )
6) Adjust buffer size for each files. ( 0 is max accuracy but so heavy. )
2) Select interface ID
for UART: COMPort#
for FTDI2xxx: FDTI ID#

## Slide 18: Trouble Shooting for MAmi
If you noticed “sound lag” or “stutter”, open the Settings dialog from [TOOL] menu. Check [Sound Type] and [Audio Latency] value.