## Slide 1: MAmidiMEmo The Virtual S/W Synthesizer
User’s Manual – for MAmidiMEmo V4.5.5.0

## Slide 2: What is the MAmidiMEmo?
MAmidiMEmo is a virtual chiptune sound MIDI module for Windows
You can use MIDI or DAW to sound the MAmi
MAmi supports various sound chips*
Also, MAmi can drive real hardware chips* via SCCI, VSIF
- DAW
- MIDI Sequencer
- Tracker
- MML and so on…
- MIDI Inst
* Supported chips are the following
PCM: C140, SPC700
FM Synthesis: OPM, OPN2, OPNA, OPLL, OPL, OPL3
WSG: NAMCO CUS30, HuC6280, SCC
PSG: SID, POKEY, GB APU, SN76496, NES APU, MSM5232, AY-3-8910
VOICE: TMS5220, SP0256, SAM
MIDI: MT-32, CM-32P(Simulation)
YM2612
YM2612
YM2612
S/W Chips
YM2612
YM2612
YM2612
Real Chips
Sound Driver
SCCI/VSIF
* Supported hardware is the following
VSIF: Genesis, SMS, Famicom, MSX, C64
SCCI: OPM, OPNA, OPZ

## Slide 3: Install & Basic Settings
Install
  Extract the downloaded zip file.
  Click MAmidiMEmo.exe
  Will open the MAmidiMEmo. If not, please check the followings.
    .NET Framework 4.7 or later installed on your PC.
    VC++ 2012 Runtime installed on your PC.
    (Execute "DelZoneID.ps1“ to remove “Zone.Identifier” flag.)

## Slide 4: Window Overview
MIDI IN A,B
Selector
Active Chips
(see next)
Chip Parameter Editor
(see next)
Tools

## Slide 5: Add and Remove a Chip
To add
Select the chip from this menu.
To remove
Open a context menu and select.

## Slide 6: Edit chip and sound parameters
1. Click chip
2. Click parameter
3. Change value

## Slide 7: Between MIDI ch and Chip ch Relation.
You don’t need to concern the Chip ch. , generally. MAmidiMEmo will assign suitable Chip ch. automatically. However, you need to concern a max ch. number of the Chip.
MAmidiMEmo will assign oldest sounding ch. to sound the new sounds.
Note On Msg from
MIDI ch. X
Chip A
FM ch. 1
FM ch. 2
FM ch. 3
MAmidiMEmo
MAmidiMemo will assign empty ch. or oldest sounsing ch. , generally.

## Slide 8: Sounding Structure
MAmidiMEmo outputs a sound from MIDI message along with the following structure. So, at least, you need to edit the Timbre parameters to sound something.
Chip X
MIDI IN
Chip A
[MIDI]-[MidiPort]
[MIDI]-[Channels]
[MIDI]-[ProgramAssignments]
[MIDI]-
[ChannelTypes]
Timbre
CombinedTimbre
DrumTimbre

## Slide 9: Timbre
Generally, a chip has 256 Timbres, 256 CombinedTimbres, 128 DrumTimbres.
CombinedTimbre can sound multiple Timbers at the same time (up to 4)
DrumTimbre can sound Timbes as a Drum sounds (Ignoring Note Off msg).
You can change the Timbre parameters on the Chip Parameter Editor. Generally, you need to learn the chip specification to edit the chip parameters.
Chip Parameter Editor

## Slide 10: Timbre Structure
Chip
CombinedTimbre
Timbre
Timbre
Timbre
Timbre
Timbres
DrumTimbre
Timbre
DrumTimbres
Timbre
CombinedTimbres
Timbre
Timbre
Timbre
Timbre
Sound parameter
Driver parameter
MIDI parameter
Sound parameter
FM Op parameters
PSG parameters
PCM parameters
Driver parameter
ADSR parameter
ARP parameter
Fx & Env parameter
Sound params are H/W settings.
See the chip manual for more details.
Driver params are the MAmidiMEmo settings.

## Slide 11: Driver parameters - Fx & Env Structure
Fx & Env parameter
Volume Env
Pitch Env
Arp Env
Dedicated Env
Click here to open the GUI Editor.
You can make for a rich sound by using driver params. Especially, FxS can do it.

## Slide 12: Sample sounds
There are sample sound files in the “Samples” folder. You can drop a sample file “*.MAmi" to the left pane.

## Slide 13: Additional files
YM2608
  Place legitimate “ym2608_adpcm_rom.bin” file in the MAmidiMEmo directory to sound ADPCM rhythm sounds.
MT-32
  Place legitimate “MT32_CONTROL.ROM” and “MT32_PCM.ROM” in the MAmidiMEmo directory to sound ADPCM sounds.

## Slide 14: Limit Break
Any chip can output only a few voices. However, MAmidiMEmo can break this limitation by the following steps.
  Add a chip and complete all settings the chip.
  Select the [Clone selected chip] Cloned chip added.
  Select the cloned chip and set the [Follower Mode] value to “Unit0*”. * If clone source chip ID is 0.
When the clone source chip consumed all voices, the cloned chip sound for the chip.
If you want to extend max voices more, select the [Clone selected chip] of the cloned chip. And set the [Follower Mode] value to “Unit0”.

## Slide 15: VGM Sound Interface(VSIF - UART) for Genesis/SMS
MAmidiMEmo and VGMPlayer can drive real machine chips. Currently supports NTSC SMS(2, MkⅢ) for SN76489, OPLL and NTSC Genesis(MD) for SN76489, OPN2.
How to
  Buy the following parts. ・1x UART dongle (Note: FT232R and so on. CH340 and CP2102 may not work 163,840bps, only 115,200bps.) ・1x FLASH Cart for SMS or Genesis and 1x D-SUB 9 pin female connector and DuPont wires
  Solder like the following and connect it to the JOYSTICK PORT 2.
SMS/2 or MkⅢ
Genesis/MD
*Need to support
163,840bps for MD
115,200bps for MD, SMS
Any UART dongle
Do not
short any pin.

## Slide 16: VGM Sound Interface(VSIF - FTDI) for Genesis
MAmidiMEmo and VGMPlayer can drive real machine chips more faster if you use FTDI2xx(232R, 232H and so on). Currently supports NTSC Genesis(MD) for SN76489, OPN2.
How to
  Buy the following parts.
    ・1x FTDI2XX dongle (FT232R and so on. Need to support 5V.) ・1x FLASH Cart for Genesis and 1x D-SUB 9 pin female connector and DuPont wires
  Solder like the following and connect it to the JOYSTICK PORT 2.
Genesis/MD
Any FTDI2XX dongle
DTR
DSR
DCD
Do not
short any pin.

## Slide 17: VGM Sound Interface(VSIF - FTDI) for Famicom
MAmidiMEmo can drive real machine chips more faster if you use FTDI2xx(232R, 232H and so on). Currently supports NTSC Famicom and RP2A03(No DAC)/FDS/VRC6.
How to
  Buy the following parts.
    ・1x FTDI2XX dongle (FT232R and so on. Need to support 5V.) ・1x FLASH Cart for Famicom and 1x D-SUB 15 pin female connector for FC and DuPont wires
  Solder like the following.
Famicom
Any FTDI2XX dongle
DTR
Audio
(Optional)
Do not
short any pin.

## Slide 18: VGM Sound Interface(VSIF - FTDI) for MSX
MAmidiMEmo can drive real MSX machine chips if you use FTDI2xx(232R, 232H and so on). Currently supports NTSC MSX for AY-3-8910 and OPLL and SCC+ and OPL3. NOTE: Be sure to select proper SLOT# for SCC to use SCC. Set FTDI clk value to 17~ for each chip.
How to
  Buy the following parts.
    ・1x FTDI2XX dongle (FT232R and so on. Need to support 5V.) ・1x D-SUB 9 pin female connector and DuPont wires
  Solder like the following and connect it to the JOYSTICK PORT 2.
MSX
Any FTDI2XX dongle
DTR
DSR
Do not
short any pin.

## Slide 19: VGM Sound Interface(VSIF - FTDI) for Commodore 64(C64)
MAmidiMEmo can drive real MSX machine chips if you use FTDI2xx(232R, 232H and so on). Currently supports NTSC/PAL C64 for SIDs.
How to
  Buy the following parts.
    ・1x FTDI2XX dongle (FT232R and so on. Need to support 5V.) ・1x D-SUB 9 pin female connector and DuPont wires
  Solder like the following and connect it to the JOYSTICK PORT 2.
  We recommend to use ARMSID with ADSR bud fixing.
C64
Any FTDI2XX dongle
DTR
DCD
RI
Do not
short any pin.

## Slide 20: VGM Sound Interface(VSIF) Settings
Burn VGMPlay_md.bin(for Genesis) or VGMPlay_sms.sms(for SMS) or VGMPlay_nes*.* (for Famicom) or VGMPlaymsx.rom(for MSX*) or VGMPlay_c64.prg to your FLASH Cart and so on.
  *VGMPlay_nes_vrc6/fds/mmc5 ROM does not show any screen but same UI with VGMPlay_nes.nes UI *VGMPlaymsx_Vkey.rom can skip booting from this ROM while the [V] key is NOT pressed at boot time.
Set the COMPort/FTDI ID and select “VSIF ***” you wish.
Reset your console and push [Panic!] button
(Famicom only)Re-send DPCM data.
Done!
If you can not sound sounds, make sure soldering and COMPort name. Or, please contact me. *Some UART dongles may not work properly. *Compatible consoles may not work properly.

## Slide 21: VGM Sound Interface(VSIF) for Famicom spec
Sound | Normal ROM (Mapper 0) | FDS IMAGE*2 | VRC6 ROM*2 (Mapper 24) | MMC5 ROM*2*3 (Mapper 5)
Square | OK | OK | OK | OK
Tri | OK | OK | OK | OK
Noise | OK | OK | OK | OK
DPCM | NO | OK(Up to 8KB) | NO | OK*1 (Up to 64KB)
Ext. Snd FDS | NO | OK*1 | NO | NO
Ext. Snd VRC | NO | NO | OK*1 | NO
Ext. Snd MMC | NO | NO | NO | NO
*1 Not Tested
*2 China flash cart may not work properly
*3 PRG-RAM 32x2 KB

## Slide 22: VGMPlayer
Select interface type
NOTE: Bandwidth of UART is narrow. So you can not play heavy track data properly.
3) Check to connect
NOTE: If you re-connect to FTDIxxx mode, please reset Gen/MD.
5) Adjust CLK speed for FTDIxxx mode for each environment (7～8% is best for normal machine)
6) Adjust buffer size for each files. (0 is max accuracy but so heavy.)
2) Select interface ID
for UART: COMPort#
for FTDI2xxx: FDTI ID#

## Slide 23: Use CMI8738(OPL) Board *NO WARRANTY*
Attach the CMI8738 Board to your PC. *Only for 64bit Windows*
Disable Driver Signature enforcement
(*Uninstall and remove* old CMI8738 OPL3 driver if installed. )
Install the CMI8738 OPL3 driver located in “.\CMI8738OPL3” folder.
Set [SoundEngine] prop to the “Real(CMI8738)”.
Have fun!!
*Technical information* If you want to use the OPL3 of the CMI8738 directly from your app…
Use the helper DLL “CMI8738OPL3Library.dll”.
Or, direct access I/O port with admin rights. eg) DF00H+50H is the OPL3(CMI8738) port.

## Slide 24: Trouble Shooting for MAmi
If you noticed “sound lag” or “stutter”, open the Settings dialog from [TOOL] menu. Check [Sound Type] and [Audio Latency] value.

## Slide 25: MIDI Implementation Chart 1
Function | Transmitted | Recognize | Remarks
Basic Channel | - | 1-16: Defaut 1-16: Changed | 
Note Number* | - | 0-127 | 
Velocity* | - | Yes: Note ON No: Note OFF | 
After Touch | - | No | 
Pitch Bend* | - | Yes | 8192: Default
Program Change | - | 0-127 | 0: Default
*Depends on the chip

## Slide 26: MIDI Implementation Chart 2
Function | Transmitted | Recognize | Remarks
Control Change 1 | - | Modulation | 0: OFF, 64: ON
5 |  | Portamento Time | 0: Default
6 38 |  | Data Entry MSB Data Entry LSB | 
7 |  | Volume* | 127: Default
10 |  | Panpot* | 64: Default 0: Left, 127: Right
11 |  | Expression* | 127: Default
16-19 |  | GPCS1 | Modify params
64 |  | Hold 1 | 0: OFF, 64: ON
65 |  | Portamento | 0: OFF, 64: ON
*Depends on the chip

## Slide 27: MIDI Implementation Chart 3
Function | Transmitted | Recognize | Remarks
Control Change 70-75,79 | - | SCCS | Modify current timbre params
76 77 78 | - - - | Mod. Rate Mod. Depth Mod. Delay | 64: Default 64: Default 64: Default
80-83 | - | GPCS2 | Modify parameters
84 | - | Portamento Ctrl | 0: OFF, 64: ON
91-95 | - | VST Plugin Ctrl | Modify VST params
98 99 | - - | NRPN LSB NRPN MSB | 
100 101 | - - | RPN LSB RPN MSB | 
*Depends on the chip

## Slide 28: MIDI Implementation Chart 4
Function | Transmitted | Recognize | Remarks
Control Change 121 | - | Reset All Ctrl | 
126 | - | Mono Mode | 0: OFF 1-127: Max Voice Num.*
127 | - | Poly Mode | 0: OFF 1-127: Reserve Voice Num.* *Reset Mono Mode when set
*Depends on the chip

## Slide 29: MIDI Implementation Chart 5
Function | MSB | LSB | Remarks
RPN | 0 | 0 | Pitch Bend Range 0-2-127 [Half Note]
 | 0 | 5 | Mod Depth 0-127 [Relative]

## Slide 30: MIDI Implementation Chart 6
Function | MSB | LSB | Remarks
NRPN | 0 | 16-19 80-83 | GPCS[1-4] Value GPCS[5-6] Value 0-127
 | 0 | 70-75 79 | SCCS[1-6] Value SCCS[10] Value 0-127

## Slide 31: MIDI Implementation Chart 7
Function | Change Receiving MIDI ch. dynamically. | Remarks
NRPN | NRPN MSB Bx 63 41 … for MIDI ch(1-7) NRPN LSB Bx 62 <Device ID> ... Specify Device ID of existing instrument. DATA MSB Bx 26 <Unit No> ... Specify Unit No of the above Device ID of existing instrument. DATA LSB Bx 06 <Receiving MIDI ch(1-7) bit sets. 1=On, 0=Off> bit 6 5 4 3 2 1 0 ch 7 6 5 4 3 2 1 NRPN MSB Bx 63 42 ... for MIDI ch(8-14) NRPN LSB Bx 62 <Device ID> ... Specify Device ID of existing instrument. DATA MSB Bx 26 <Unit No> ... Specify Unit No of the above Device ID of existing instrument. DATA LSB Bx 06 <Receiving MIDI ch(8-14) bit sets. 1=On, 0=Off> bit 6 5 4 3 2 1 0 ch 14 13 12 11 10 9 8 NRPN MSB Bx 63 43 ... for MIDI ch(15-16) NRPN LSB Bx 62 <Device ID> ... Specify Device ID of existing instrument. DATA MSB Bx 26 <Unit No> ... Specify Unit No of the above Device ID of existing instrument. DATA LSB Bx 06 <Receiving MIDI ch(15-16) bit sets. 1=On, 0=Off> bit 6 5 4 3 2 1 0 ch xx xx xx xx xx 16 15 | 

## Slide 32: VSIF – Generic (UART 115K), SMS(UART 115K) SPECIFICATION for AY-3-8910, YM2413
Baud rate: 115,200 bps
Protocol: 8 bits, None parity bit, 1 stop bit
1 packet : 2 bytes
Reg #
Value
1st
2nd

## Slide 33: VSIF – MSX(FTDI) SPECIFICATION for AY-3-8910, YM2413, SCC-I, YMF262
Baud rate : 38,400 bytes / sec
1 packet : 5 bytes + α
1byte : 4bit(data) + 2bit(Start + Clk bit)
Type:
  0 AY-3-8910: Write value to address
  1,2 YM2413: 1 is write value to address, 2 is set OPLL cartridge slot number
  3～9 SCC-I: (in preparation)
  10～11 YMF262: 10 is write value to address of port L , 11 is Write value to address of port H
Address(Hi)
Address(Lo)
Value(Lo)
Value(Hi)
Type
1st(Start)
2nd(clk=0)
3rd(clk=1)
4th(clk=0)
5th(clk=1)
1
Type
Type
Type
Type
Type
LSB
0
MSB
7
0
clk
Data
Data
Data
Data
Start
Clk
…

## Slide 34: VSIF – C64(FTDI) SPECIFICATION for SID
Baud rate : 31,250 bytes / sec
1 packet : 6 bytes(1 byte value) or 9 bytes (2 bytes value) mode
1byte : 3bit(data) + 2bit(Start(Active low) + Clk(Active low) bit)
9 bytes mode flag:
Address(Lo 3bit)
Address(Mid 3bit)
Value(Hi 3bit)
Value(Mid 3bit)
1st
2nd
3rd
4th
5th
Start
Clk
Data
Data
Data
LSB
0
MSB
7
Address(Hi 2bit)
Value(Lo 2bit)
6th
Start
Clk
9bytes flag
Data
Data
LSB
0
MSB
7
6th byte data
Value(Hi 3bit)
Value(Mid 3bit)
Value(Lo 2bit)
7th
8th
9th
…
7~9th
NOTE: In 9bytes mode, send value for Address+1 data first, second is Address+0 data
7~9th byte data
Same as 4,5,6 th

## Slide 35: Integrate with MAmidiMEmo via RPC
MAmidiMEmo will starts RPC server on port 30000 at startup. So, your application can be integrate with the MAmidiMEmo via RPC. MAmidiMEmo provides the following API //Write the value to the address to the specific chip void DirectAccessToChip(unsigned char DeviceID, unsigned char UnitNo, unsigned int address, unsigned int data) * You can confirm the DeviceID and UnitNumber from the property. * Currently, OPLL(ID9), SCC(ID7), AY8910(ID11) chips are supported. * If you want to use SCC1(aka SCC+), you need to add 0x100 to the address.
Ex)
rpc::client* m_rpcClient = new rpc::client("localhost", 30000); //Open RPC port
:::
//Write SCC1 wave form
m_rpcClient->async_call("DirectAccessToChip", (unsigned char)7, (unsigned char)0, (unsigned int)0x100, (unsigned int)10);
//All sound off for AY8910
m_rpcClient->async_call("DirectAccessToChip", (unsigned char)11, (unsigned char)0, (unsigned int)7, (unsigned int)0x3f);
//Key off 1ch for OPLL
m_rpcClient->async_call("DirectAccessToChip", (unsigned char)9, (unsigned char)0, (unsigned int)0x20, (unsigned int)0x0);
:::
m_rpcClient->~client(); //Close RPC port